## Slide 1
Team Members
Aswin Raaj .R
Mani Balaji .S
Tharun .V.S
Guided by
Dr.G.Pandiaraj
Assistant Professor (Sl. Grade)
Electrical and Electronics Engineering
Badminton Swing Analyzer
using
MPU6050
Batch –B2

## Slide 2
To design a low-cost badminton swing analyzer utilizing
MPU6050 and ESP32 MCU
To support players in improving their skills through measurable swing parameters and visual feedback of performance
Problem Statement:
Players lack affordable swing analytics tools
Existing solutions are costly
Objective:

## Slide 3
Working of MPU 6050
IMU – Measures body's specific force, angular rate, using accelerometers, gyroscopes .Used in robotics, aerospace, and motion tracking in sports
MPU6050 uses MEMS technology - 6 axis motion tracking device( 3-axis accelerometer, 3-axis gyroscope, temperature sensor and DMP)
Accelerometer – measures(static and dynamic acc) , capacitive sensing – variation of C = applied acc.
AD: high accuracy, low power consumption

## Slide 4
Similar sensors: ADXL345 , MPU9250
MPU6050 sensor
Gyroscope – measures orientation and ang.V, Variation of C= applied ang.rate
Follows Coriolis Effect . Have 4 proof mass – detect roll(x) ,pitch(y), yaw(z)
When mass moves in spec. direction with V and ext. ang. Rate applied – produce -Coriolis Effect .- generates a force – moves in perpendicular direction

## Slide 5
Research papers overview
S.no | 1 | 2
Research Paper Title | Design of angle detection system based on MPU6050 | Vibration detection prototype Using MPU6050
Key findings | Effective in detecting angles | Effective in detecting vibrations
Limitation | Need for calibration in different conditions | Interference of noise
What we improve in our project | Get offset values of racket position by keeping it stable for 3s (approx. 3000samples) | Using Kalman filter, reduce sensor drift and noise interference
http://www.jurnal.nips.ru/sites/default/files/A&SE-1-2015-11_0.pdf
https://ijsrst.com/home/issue/view/article.php?id=IJSRST52310620

## Slide 6
Calibration of sensor

## Slide 7
Block Diagram

## Slide 8
Swing Metrics to be measured
S.no | Swing Metrics | Need
1. | Swing speed (km/hr) – from acc.data | To measure swing speed
2. | Peak angular velocity(deg/s) – from gyro.data | To measure fastness of swing
3. | Impact force (m/s^2) | Solidness of the hit

## Slide 9
S.no | Components | Weight in g | Price(rs) (approx.)
1. | MPU6050 sensor | 3-4 | 500
2. | ESP32 DEVKIT V1 | 10 | 600
3. | TP4056 Charging Module | 3-5 | 50
4. | 3.7V 1000mAh Li-po Battery | 20 | 300
5. | Badminton Racket -Hardware | 80 | 
 | Total | 80+36=116g | 1450rs
Bill of Materials and Cost
Approx. price = 1500rs

## Slide 10
Prototype Design
MPU 6050
ESP32 MCU and 3.7V Li-Po battery
TP4056 charging module

## Slide 11
Swing Speed Graph

## Slide 12
Angular Velocity Graph

## Slide 13
Impact Force Graph

## Slide 14
Session Summary

## Slide 15
Sensor Drift and Noise interference
Power Consumption
Calibration complexity
Challenges

## Slide 16
Gantt Chart

## Slide 17
References
Rodrigues, João Victor Oliveira, et al. "Performance evaluation of accelerometers ADXL345 and MPU6050 exposed to random vibrational input." Research, Society and Development 10.15 (2021): e286101523082-e286101523082.
Fedorov, D. S., et al. "Using of measuring system MPU6050 for the determination of the angular velocities and linear accelerations." Automatics & Software Enginery 11.1 (2015): 75-80.
Jacob, Alvin, Wan Nurshazwani Wan Zakaria, and Mohd Razali Bin Md Tomari. "Implementation of IMU sensor for elbow movement measurement of badminton players." 2016 2nd IEEE International Symposium on Robotics and Manufacturing Automation (ROMA). IEEE, 2016.
Li, Li, and Feng Li. "Recognizing badminton hitting movements Based on Multi-sensor trajectory recognition algorithm." 2023 3rd International Conference on Information Technology and Contemporary Sports (TCS). IEEE, 2023.
https://ijsrst.com/home/issue/view/article.php?id=IJSRST52310620
https://pubmed.ncbi.nlm.nih.gov/38580698/
http://www.jurnal.nips.ru/sites/default/files/A&SE-1-2015-11_0.pdf

## Slide 18
Thank You